## Slide 1
Working Principle of Timers & Splitters
How hardware counts time, generates events, and captures snapshots — with a practical VHDL stopwatch example.
Group Members :
HARISH - 2620080071
NEERAJ - 2620080074
SNEHA- 2620080080
SANTHOSHI - 2620080081
TANUSH - 26200800120

## Slide 2
Why Timers Exist: Software Delays Aren't Time
Software loops are unreliable for measuring time — interrupts and CPU load introduce unpredictable delays. A hardware timer is a dedicated counter driven by a stable clock, so you know precisely when a fixed interval has elapsed, regardless of what the CPU is doing.
Software Delay
Unreliable under interrupts or heavy CPU load
Hardware Timer
Dedicated counter, independent of CPU activity

## Slide 3
The Core Loop: Clock → Count → Compare → Event
Event
Compare
Counter
Clock
The timer accumulates ticks from a chosen clock source. When the count reaches a preset threshold — or overflows — hardware raises an event flag, allowing your program to respond precisely. Designers trade resolution against range by selecting the clock frequency and prescaler.

## Slide 4
SPLITTER CONCEPT
One Time Source, Multiple Views
A splitter lets you freeze a displayed value while the internal time generator keeps counting. Conceptually:
time_gen
Continuously updates counter value N
diload (split toggle)
When low, DI stops loading new values — display freezes

## Slide 5
The 555 Timer: Time from Charge & Discharge
The classic 555 timer IC produces precise timing intervals using an external capacitor and resistors. Internal comparators monitor the capacitor voltage, and an RS flip-flop switches the output state when thresholds are crossed.
Charge Phase
Capacitor voltage rises through R until it hits ⅔ VCC (upper threshold)
Discharge Phase
Flip-flop toggles; capacitor discharges until it hits ⅓ VCC (lower threshold)
Output Switch
RS flip-flop drives output HIGH or LOW based on comparator states

## Slide 6
555 Modes: Direct Mapping to Timer Behaviours
Each mode maps to a distinct timer behaviour:
1
Monostable
Single pulse on trigger — ideal for one-shot delays
2
Astable
Continuous oscillation — RC cycles repeat indefinitely
3
Bistable
Latch behaviour — output holds until reset

## Slide 7
Practical Example: VHDL Stopwatch with Split
A VHDL stopwatch demonstrates both principles working together — a running time generator and a display latch for split timing.
time_gen
Counters generate elapsed time digits continuously from clkin
BTN(1) — Pause
Toggles clkin to pause time_gen internally
BTN(2) — Split
Drives diload low; DI stops loading, freezing the display
Result
Visible split captured while time keeps running — timer + splitter in action

## Slide 8
Key Takeaways
Timers Control WHEN
They manage precise timing and trigger actions at exact moments
Splitters Control WHERE
They distribute signals to multiple destinations simultaneously
✓
Together They Enable Control
Combined, they create synchronized multi-output systems for real-world applications
CONCLUSION
Understanding timers and splitters is fundamental to modern electronic control systems and automation.
TIMERS & SPLITTERS
9

## Slide 9
THANK YOU
ANY QURIES….